## Slide 1
Lecture 03 - Morphology
Prof. André Gustavo Hochuli
gustavo.hochuli@pucpr.br
aghochuli@ppgia.pucpr.br
Notes: Prof. André Hochuli

## Slide 2
Topics
Computer Vision - Prof. André Hochuli
Lecture 03
Discussion of Practice 02
Mathematical Morphology
  Structuring Element (or Kernel)
  Erode /Dilate
  Open / Close
  Gradients
  Watershed
Practice
Notes: Prof. André Hochuli

## Slide 3
Mathematical Morphology
Computer Vision - Prof. André Hochuli
Lecture 03
Morphology (Nature): Branch of Biology that study the form and structure of animals and plants
Morphology (Image Processing): Mathematical operations to extract image components based on pixel neighborhood.
Increase/Decrease Objects Size, Reduce Noise, Closing or Open (GAPS)
Notes: Prof. André Hochuli

## Slide 4
Structuring Element (Kernel)
Computer Vision - Prof. André Hochuli
Lecture 03
Defines the shape of the structure to be applied
The structure is slid through the image
Erosion or Dilate operations are applied
The origin determines the pixel be changed
Notes: Prof. André Hochuli

## Slide 5
Erosion
Computer Vision - Prof. André Hochuli
Lecture 03
Moves one’s to zero’s
Binary ‘AND’ Operation
Reduces Noises and Contours
Notes: Prof. André Hochuli

## Slide 6
Dilation
Computer Vision - Prof. André Hochuli
Lecture 03
Moves zero’s to one’s
Binary ‘OR’ Operation
Increases Objects, connects contours, and fill holes.
Notes: Prof. André Hochuli

## Slide 7
Opening and Closing
Computer Vision - Prof. André Hochuli
Lecture 03
Combined morphological operations that preserve the shape and size o large objects in the image
  Opening: Erode + Dilate
    Removes small objects, noises, and thin lines
  Closing: Dilate + Erode
    Fill small holes and connect segmented contours
Notes: Prof. André Hochuli

## Slide 8
Others Morphological Operations
Computer Vision - Prof. André Hochuli
Lecture 03
Gradient: Dilate - Erosion
  Outline de Object
TopHat: Open – Original Image
  Reduce the effect of brightness changes
  Isolates brightness objects
Notes: Prof. André Hochuli

## Slide 9
Let’s code!
Computer Vision - Prof. André Hochuli
Lecture 03
Link: Morphology Operators
Notes: Prof. André Hochuli